## Slide 1: 

## Slide 2: 
Earthwork includes:
1. Excavation
2. Grading: Moving earth to change elevation
3. Temporary shoring
4. Back fill or fill: Adding earth to raise grade
5. Compaction: Increasing density
6. Disposal

## Slide 3: 
A. Job conditions
  Material type
  Water level and moisture content
  Job size
  Length of haul
  Haul road condition (accessibility and load restrictions)

## Slide 4: 
B. Management conditions
  Equipment conditions and maintenance practices
  Skills of work force and management
  Planning, supervision and coordination of work.

## Slide 5: 
Notes: 7

## Slide 6: 
Cubic Yard (bank, loose, or compacted)

## Slide 7
1.0
1.25
0.90
1.0 CUBIC YARD IN NATURAL CONDITION (IN-PLACE YARD)
1.25 CUBIC YARD AFTER DIGGING (LOOSE YARDS)
0.90 CUBIC YARD AFTER COMPACTED (COMPACTED YARDS)
In place
Compacted
Loose
Notes: 6

## Slide 8: 
Bank: VB
  Bank cubic yards (BCY)
  Density B Lb /BCY
Loose: Vl
  Loose cubic yards (LCY)
  Density L Lb/LCY
Compacted: Vc
  Compacted cubic yards (CCY)
  Density C LB/CCY

## Slide 9
Swell:
  A soil increase in volume when it is excavated.
Swell (%) = ( - 1) x 100
Load factor =
Bank Volume = Loose volume x Load factor
Loose density
Bank density
Bank density
Loose density

## Slide 10
Shrinkage:
A soil decreases in volume when it is compacted
Shrinkage (%) = (1 - ) x 100
Shrinkage factor = 1 - Shrinkage
Compacted volume
= Bank volume x Shrinkage factor
Bank density
Compacted density

## Slide 11: 
Exact values will vary with grain size, moisture content, compaction, etc. Test to determine exact values for specific soils.

## Slide 12: 

## Slide 13: 
Angle of Repose
2’-0”
or more

## Slide 14: 
For Sloping Sides of Excavation
Original
Ground Line
Solid Rock, Slate or Cemented Sand and Gravel
(90 Deg.)
Compacted Angular Gravels
1/2:1 (63 Deg.)
Recommended Slope for Average Soils
1:1 (45 Deg.)
Compacted Sharp Sand
1 1/2 :1 (33 Deg.)
Well Rounded Loose Sand
2:1 (26 Deg.)

## Slide 15: 
1. End Area Method
2. Contour Line/ Grid Method

## Slide 16: 
Used in sites where length is much greater than width

## Slide 17: 
1. End Area Method
a. Take cross-sections at regular intervals, typically, 100’ intervals.
b. Calculate the cross-section end areas
c. The volume of earthwork between sections is obtained by taking the average of the end areas at each station in square feet multiplied by the distance between sections in feet and dividing by 27 to obtain the volume in cubic yards.

## Slide 18: 
Fill
Cut
80
82
84
86
88
80
84
86
88
82
78
A’
B’
C’
D’
E’
F’
A
B
C
D
E
F
100'
100'
100'
100'
100'
500'
300'
Notes: 2

## Slide 19
80
78
76
82
80
78
84
82
80
86
84
88
86
90
88
78.5
80.3
82.3
84.2
86.2
88.2
Sec. A’- A
Sec. B’- B
Sec. C’- C
Sec. D’- D
Sec. E’- E
Sec. F’- F
Project Cross Sections
Notes: 3

## Slide 20: 
80
79
78
77
76
79.5
78.5
76.7
Section A’- A
Area = = 173.7
193 x 1.8
2
Area = = 53.5
107 x 1.0
2
Notes: 4

## Slide 21: 
82
81
80
79
78
81.8
80.3
76.7
Section B’- B
Area = = 189.0
210 x 1.8
2
Area = = 67.5
90 x 1.5
2
Notes: 5

## Slide 22: 

## Slide 23: 
Used for parking lots and site “leveling”
Grid size from 10’x10’ to 50’x50’
the greater the terrain variance the smaller the grid

## Slide 24: 
Step l
Determine by visual study of the site drawing if the net total will be an import (more fill required than cut) an export (less fill required than cut) or a blend (cut and fill about equal)
Step 2
Determine the pattern of calculation points or grid size.
Step 3
Determine elevations at each calculation location, the corners of each grid.
Step 4
Calculate the cubic yards of cut or fill required in each grid cell.
Step 5
Add the individual Grid Cell quantities together to arrive at the total cut, total fill volume and the import or volume export yardage required for the job.

## Slide 25
A
B
C
D
E
F
87.6
88.6
89.4
90.4
91.6
93.2
G
H
J
K
L
M
87.4
88.2
89.5
90.6
91.6
92.7
N
O
P
Q
R
S
87.2
87.7
89.0
90.4
91.3
92.0
87.6
88.5
89.3
90.3
91.5
95.0
94.3
93.5
93.1
A
B
C
D
E
F
G
300’
88’
89’
90’
91’
92’
93’
94’
No Scale
Notes:
1. Bring the entire site to elevation 90.
2. All grids are 50’x 50’ = 2500 sq. ft.
3. Present contours
Notes: 9

## Slide 26
Purpose
Grade the entire site to grade 90’
Quick and Dirty
Assume one grid
Existing 90.50
Proposed 90.00
Cut 0.50
Total Cost = = 833CY
150 x 300 x 0.50
27
300'
150'
Need
Fill
Need
Cut
90'
90'
91'
90.5'

## Slide 27
Average elevation
=
= 88.08
change = 90-88.08
= 1.92
cut =
= 177.77 CY
and so on.
If we choose the grid size to be 50’x50’
87.6+88.5+87.6+88.6
4
87.6
88.6
87.6
87.6